ILI9341 240x320 2.2” TFT display

This project aims to create a display driver for the ILI9341 display module issued along with the University of Southampton Il Matto boards.

We are using an 8-bit Parallel Interface (Type 1) to communicate with the display

System Interfaces
- 8/9/16/18-bit interfaces with 8080 series MCU
- 6/16/18-bit RGB interface with Graphic Controller
- ¾ line serial interface

Pins on Il Matto board:
- CS	Chip Select (active low)
- BLC	Backlight Control (active low?)
- RESET	Reset (active low)
- WR	Data Write Strobe (rising edge)
- RS	Data(1)/Command(0) selection
- RD	Data Read Strobe (rising edge)
- VSYNC	VSYNC
- FMARK	Frame Mark
- D[7:0]	Data Bus

This is an Asynchronous process, which is nice as it lets us take our time. I am curious as to how fast we can clock our FPGA side though.
# Timing Requirements

Frame Memory (FM) reads are much much slower than Register reads (ID)

# Interfacing
## Write Cycle Sequence
# Read Cycle Sequence
## Using VSYNC
If the ILI9341 is in VSYNC mode, the VSYNC pin will control the framerate, and it will stall writes to the GRAM until a few lines after the falling edge of VSYNC to ensure no screen tearing is visible.
See the datasheet section 7.3 (page 52) for more details.

## Display Data Format
Depending on if we want 16 bit colour or 18 bit colour, we have different options:
Using 16bpp, we have faster transfers but they are somewhat less intuitive as we are splitting the colours across different transfers (in practice, won’t be a problem in VHDL)
Using 18bpp, we have neater transfers with Red, Green and Blue in their own separate transfers, but we take 1 more cycle per pixel which is a big bandwidth reduction.

# Command Reference
## Initialisation
These are the commands send by ili9341_init in ili9341.h from the Il Matto library
### Initial Conditions and Hardware Reset
TFT_PCTRL = 0xFF & ~TFT_FMK;	// Set FMARK as input pin
TFT_WCTRL = 0xFF & ~TFT_BLC;    // Disable background light

RECV();	//Switch DATA port to INPUT and enable pullups

// Hardware Reset
LOW(TFT_RST);        	// Assert Active Low Reset
LOW(TFT_CS);	// Assert Active Low Chip Select
HIGH(TFT_WR);	// Put the Read/Write Strobes HIGH
HIGH(TFT_RD);
HIGH(TFT_RS);	// Put the IO bus in Data Mode
HIGH(TFT_VSY);	// Put VSYNC HIGH
_delay_us(10);          // Min: 10us delay for hardware reset
HIGH(TFT_RST);	// deassert RESET pin
_delay_ms(120);	// wait until we are fully out of reset

### Software Setup

SEND();	// Switch DATA port to OUTPUT
ili9341_cmd(0x28);      // Display OFF
ili9341_cmd(0x11);      // Exit Sleep Mode
_delay_ms(120);
ili9341_cmd(0x34);      // Tearing Effect Line OFF
ili9341_cmd(0x38);      // Idle Mode OFF
ili9341_cmd(0x13);      // Normal Display Mode ON
ili9341_cmd(0x20);      // Display Inversion OFF
ili9341_cmd(0x3A);      // COLMOD: Pixel Format Set
ili9341_data(0x55);     // 16 bits/pixel
ili9341_cmd(0x36);      // Memory Access Control
ili9341_data(0x48);     // Column Adress Order, BGR
ili9341_cmd(0x2C);      // Memory Write
for (r = 0; r < 320; r++)   // Black screen
    for (c = 0; c < 240; c++) {
        ili9341_data(0x00);
        ili9341_data(0x00);
        ili9341_data(0x00);
    }
ili9341_cmd(0xB1);      // Frame Rate control, normal
ili9341_data(0x00);     // 70Hz
ili9341_data(0x1B);
ili9341_cmd(0xB3);      // Frame Rate control, partial
ili9341_data(0x00);     // 70Hz
ili9341_data(0x1B);
ili9341_cmd(0x29);      // Display On

## Commands

COLMOD Settings (0x3A) Pixel Format Settings
we write 0x55 (16-bit colour) or 0x66 for 18-bit colour
0x2C Memory Write
This starts the writing of memory to the framebuffer

# Pinout
ILI9341 Datasheet Pin	Direction	Il Matto Display Schematic Pin	Description
IM[3:0]	I	IM[3:0] (GND)	MCU Interface Mode
RESX	I	RESET	Active Low Reset
EXTC	I	Unused/NC?	Extended Command Set Enable (extended commands not available)
CSX	I	CS	Active Low Chip Select
D/CX	I	RS	Data/Command Select
RDX	I	RD	Read Strobe (rising)
WRX	I	WR	Write Strobe (rising)
D[17:0]	IO	D[7:0]	Parallel Data Bus
SDI/SDA	IO	SDI (GND)	Serial Data In
SDO	O	SDO (floating)	Serial Data Out
TE	O	FMARK?	Tearing Effect Output to synchronise MPU to frame writing, activated by SW command (else LOW)
DOTCLK	I	DOTCLK (GND)	RGB Mode Pixelclk
VSYNC	I	VSYNC	VSYNC input
HSYNC	I	HSYNC (GND)	HSYNC input
DE	I	ENABLE (GND)	Data Enable Signal for RGB mode

Additionally, we have BLC on the Il Matto Display module that activates LEDK[3:1]

Controller Notes – Adding BRAM and colour conversion
We want a framebuffer BRAM that is 256x320 for easy address calculation
In portrait mode:
Address [7:0] is the column addresses X (8 bits)
Address [16:8] is the row address Y (9 bits)

What are we storing (note, we can use different read/write widths if thats what we want):
Lets start with 8 bit colour (3-3-2 RGB) to nicely match with processors
## Scaling 8 bit to 16 bit (5-6-5 RGB)
### Red
3 bit 0-7 to 5 bit 0-31
### Green
3 bit 0-7 to 6 bit 0-63

### Blue
2 bit 0-3 to 5 bit 0-31